## Slide 1
OE Fuel Pump
6AN Pump Adapter
100μm Summit Filter
10μm Radium Filter w/ heatsink
Fuel Pressure Regulator/Damper
6AN
Rail Adapter
6AN Rail Adapter
1/8 NPT sensor
Low Pressure Return Line
Braided PTFE 6AN Hose
Fuel Tank
Firewall
Plastic Barb
6 AN dry break fitting
6 AN dry break fitting
Plastic Barb
6 AN Hose Ends
8x
4x
4x
OE Fuel Rail
Fuel System Diagram
6AN Barb Adapter

## Slide 2
OE Fuel Pump
6AN
Rail Adapter
6AN Rail Adapter
1/8 NPT sensor
Hard Line Return ¼”
Braided PTFE 6AN Hose
Fuel Tank
Firewall
Plastic Barb
Amazon FPR
Plastic Barb
6 AN Hose Ends
2x
3x
OE Fuel Rail
Fuel System Diagram
Hard Line Feed 5/16”
6 AN to ¼ hard line compression fitting
6 AN to 5/16 hard line compression fitting

## Slide 3
Fuel System Goals: Maximize Reliability and Tuning Control
Eliminate leaks and line failures under race conditions
Replace every rubber-on-barb feed, return and vapor line with braided PTFE 6 AN hoses and proper threaded fittings for a fully flare-sealed system. Dry-break quick-disconnect fittings immediately before and after the rail allow fast engine removal.
Lower seat & minimize fuel heating and vapor lock risk from nearby exhaust
Reroute and extend all hard and soft lines outboard of the driver’s seatwell, securing them with new chassis-mount AN brackets and stainless-steel clamps. Fit a radial-mount heat sink on the fuel filter.
Steady fuel pressure through all RPM and cornering loads
Install a Radium Engineering combined adjustable fuel-pressure regulator + damper at the firewall feed bulkhead, plumbing in-6 AN inlet and outlet lines for minimal restriction.
Prevent debris and contamination from clogging injectors or reaching the newly machined engine
Fit a dual-stage inline filtration setup in the feed circuit: a 10 µm fine filter directly upstream of the fuel rail and a 100 µm coarse filter to prevent clogging.

## Slide 4
Rubber vs PTFE Comparison All Radium Engineering PTFE hoses have been successfully tested in-house to 1200psi although PTFE can typically withstand 2500psi+. They are also for extreme temperatures (-94F to +480F). They feature an extruded PTFE (fluoropolymer) core wrapped in a stainless steel wire braided sleeve. The outer coating for the universal DIY ends is braided PET. All hose ends are type-II black anodized aluminum.
How to Pressure Test Assembled Hose
AN Hose Info & Installation
How to use AN Hose Installation Tool
Connect hose ends to fittings with AN hose wrench & only clamp with vise protector
Fitting Type Overview. The White Tiburon will use a combination of AN, ORB and NPT fittings for sensor taps fuel and power steering steering. DO NOT use tape or sealant on AN or ORB fittings and DO NOIT use AN or ORB with different flare-type fittings.
AN fittings are a flare fitting, using 37° flared tubing to form a metal-to-metal seal, meet SAE Aerospace (AS) standards.
ORB fittings are Commonly knowns as the O-ring boss (ORB), these types of fittings are defined by the SAE J1926 standard. The O-ring allows for an extremely tight seal that can withstand high pressures, useful for hydraulic and other automotive applications.

## Slide 5
Power Steering Reservoir
Braided PTFE 6AN Hose
Firewall
Power Steering Pump
10 AN dry break fitting
Power Steering Diagram
Braided PTFE 10AN Hose
Steering Rack